## Slide 1: Embedded Systems Lab Prep 7 Interrupts

## Slide 2: How can we actively monitor
How can we actively monitor a sensor? Say a simple button.
We could check it periodically, but if the button is pushed between checks, we won’t know.
We can’t watch it constantly, as this means we don’t get a chance to run any other code.
So we use interrupts

## Slide 3: Interrupts
Interrupts allow you to tell the ESP32 to watch for a certain hardware or software change.
In your code, you can now go and do other things
The Arduino handles the checking for you, and when the change occurs, the Arduino will automatically jump to a function you have told it to.
There are two kinds of interrupts, hardware and software interrupts. Hardware allows you to monitor for pin changes (like a pin going from high to low) while software allows you to monitor a timer.

## Slide 4: Hardware Interrupt Implementation
Use the attachInterrupt(pin, mode, ISR).
The pin is the pin to monitor.
The mode is the state to look for, LOW, RISING (low to high), FALLING (high to low) and CHANGE.
The ISR is the interrupt service routine, or the function that is called when the interrupt is triggered. It can accept no parameters, and it cannot return anything. It should be as short and as fast as possible.
Sometimes after the interrupt is called, you want to detach it. Use detachInterrupt(pin) to do this.

## Slide 5: Timer Usage
My_timer = timerBegin(timerID, prescaler, countUp);
Above will initialize a timer.
timerID specifies which ESP32 timer to use. There are only 4 timers, so this number must go from 0-3.
The prescaler is a 16-bit number. It controls the frequency at which the timer increments. The timer frequency is the ESP 32 clock speed (80,000,000) / prescaler. So a prescaler of 80 yields 1,000,000 or 1 microsecond per tick. 80 is a good average to use.
The countUp parameter is a Boolean, which will cause the timer to count up when true, or down when false.

## Slide 6: Timer Usage Continued
Now you attach the interrupt (same as a hardware interrupt) but instead of passing the pin, use the timer object, My_timer.
You then run the timerAlarmWrite(timer, alarmValue, autoReload)
Timer is your timer object, My_timer.
alarmValue is the number of ticks until the alarm triggers. If you want one second, you would do 1,000,000 since you are counting in microseconds.
autoReload is a Boolean, true if the timer should reset automatically, and false if not.